## Slide 1
Physical Computing
with Python in the classroom
k-stulens@ti.com
cbaars@martinuscollege.nl
www.t3nederland.nl
www.wil-destem.nl
www.t3europe.eu

## Slide 2
Physical Computing …
Physical computing covers the design and realization of
interactive objects and installations and allows students to
develop concrete, tangible products of the real world, which arise from the students’ imagination – Przybylla, 2014.

## Slide 3
Physical Computing …
Physical computing covers the design and realization of
interactive objects and installations and allows students to
develop concrete, tangible products of the real world, which arise from the students’ imagination – Przybylla, 2014.
Physical computing involves interactive systems that can sense and respond to the world around them.
Physical computing is a framework for understanding human beings' relationship to the digital world.
In practice physical computing often describes design or DIY - do it yourself - projects that use sensors and microcontrollers to translate analog input to a software system and/or control hardware.

## Slide 4
Physical Computing …
Physical computing covers the design and realization of
interactive objects and installations and allows students to
develop concrete, tangible products of the real world, which arise from the students’ imagination – Przybylla, 2014.
Physical computing involves interactive systems that can sense and respond to the world around them.
Physical computing is a framework for understanding human beings' relationship to the digital world.
In practice physical computing often describes design or DIY - do it yourself - projects that use sensors and microcontrollers to translate analog input to a software system and/or control hardware.
Physical computing means interacting with real-world objects by programming: programming an LED to flash, reading environmental data from a sensor, …
Applications like these are all around us, from traffic signals to driverless cars.
Behind these applications are algorithms and programs that govern their behaviour. Physical computing is combining hardware and software in order to create something useful / productive or simply just for fun.

## Slide 5
Physical Computing …
in the classroom
TI Technology: www.education.ti.com > Select your country
TI Educational Content: www.t3europe.eu
Classroom
TI-Nspire CX Technology
TI-84 Plus CE-T python edition
TI-Innovator Hub
BBC micro:bit
Physical Environment
output
input
TI HUB Python Module

## Slide 6
Physical Computing …
in the classroom
TI Technology: www.education.ti.com > Select your country
TI Educational Content: www.t3europe.eu
Classroom
TI-Nspire CX Technology
TI-84 Plus CE-T python edition
TI-Innovator Hub
BBC micro:bit
Physical Environment
processing
outputs
inputs
system
environment
sensors
actuators

## Slide 7
Physical Computing …
in the classroom
TI Technology: www.education.ti.com > Select your country
TI Educational Content: www.t3europe.eu
Classroom
TI-Nspire CX Technology
TI-84 Plus CE-T python edition
TI-Innovator Hub
BBC micro:bit
Physical Environment
processing
outputs
inputs
system
environment
sensors
actuators
Smart Irrigation System
www.tistemprojects.com
Water Pump
Moisture sensor
resources.t3europe.eu

## Slide 8
Physical Computing …
Basics – Actuators
Flashing LED
from ti_hub import *
flash=led("BB1")
for i in range(5):
flash.on()
sleep(1)
flash.off()
sleep(1)
Sound

## Slide 9
Physical Computing …
Basics – Actuators
Sound
Flashing LED
from ti_hub import *
flash=led("BB1")
for i in range(5):
flash.on()
sleep(1)
flash.off()
sleep(1)
from ti_hub import *
sound=speaker("BB1")
for i in range(5):
sound.tone(500,1)
sleep(1)
sound.tone(375,1)
sleep(1)

## Slide 10
Physical Computing …
Basics – Actuators
Sound
Flashing LED
from ti_hub import *
flash=led("BB1")
for i in range(5):
flash.on()
sleep(1)
flash.off()
sleep(1)
from ti_hub import *
sound=speaker("BB1")
for i in range(5):
sound.tone(500,1)
sleep(1)
sound.tone(375,1)
sleep(1)

## Slide 11
Alarm
from ti_hub import *
flash=led("BB1")
sound=speaker("BB2")
for i in range(5):
flash.on()
sound.tone(500,1)
sleep(1)
flash.off()
sound.tone(375,1)
sleep(1)
Physical Computing …
Basics – Actuators
Sound
Flashing LED
from ti_hub import *
flash=led("BB1")
for i in range(5):
flash.on()
sleep(1)
flash.off()
sleep(1)
from ti_hub import *
sound=speaker("BB2")
for i in range(5):
sound.tone(500,1)
sleep(1)
sound.tone(375,1)
sleep(1)

## Slide 12
Physical Computing …
Basics – Sensors
from ti_hub import *
from ti_system import *
temp=temperature("IN 1")
while get_key() != "esc":
t=temp.measurement()
print("Temperature =",t)
sleep(0.5)
get_key()
Temperature

## Slide 13
Physical Computing …
Basics – Sensors
from ti_hub import *
from ti_system import *
temp=temperature("IN 1")
while get_key() != "esc":
t=temp.measurement()
print("Temperature =",t)
sleep(0.5)
get_key()
Temperature
from ti_hub import *
from ti_system import *
mag=magnetic("IN 3")
while get_key() != "esc":
m=mag.measurement()
print("Hallsensor = {}".format(int(m)))
if m<100:
print("Magnet detected")
else:
print("Magnet not detected”)
sleep(1)
get_key()
Magnetic Field

## Slide 14
from ti_hub import *
from ti_draw import *
flash=led("BB1")
sound=speaker("BB 2")
temp=temperature("IN 1")
mag=magnetic("IN 3")
Physical Computing …
Heat Car Alarm
Don’t let us in the car!

## Slide 15
Physical Computing …
Heat Car Alarm
Structure
Translate
Process
Control
from ti_hub import *
from ti_draw import *
flash=led("BB1")
sound=speaker("BB 2")
temp=temperature("IN 1")
mag=magnetic("IN 3")
Don’t let us in the car!

## Slide 16
Physical Computing …
Heat Car Alarm
Don’t let us in the car!
Structure
Translate
Process
Control
from ti_hub import *
from ti_draw import *
flash=led("BB1")
sound=speaker("BB 2")
temp=temperature("IN 1")
mag=magnetic("IN 3")

## Slide 17
from ti_hub import *
from ti_draw import *
flash=led("BB1")
sound=speaker("BB 2")
temp=temperature("IN 1")
mag=magnetic("IN 3")
Physical Computing …
Heat Car Alarm
Structure
Translate
Process
Control
set_color(0,0,255)
draw_text(50,80,"HEAT CAR ALARM”)
set_color(0,0,0)
draw_text(50,120,"Temperature in car = {}".format(t))
if m > 100:
draw_text(50,100,"Baby not in car")
set_color(0,100,0)
draw_text(50,140,"No problems detected")
else:
draw_text(50,100,"Baby in car")
if t > 30:
set_color(255,0,0)
draw_text(50,140,"Baby in heath distress")
flash.blink(10,1)
sound.tone(440,1)
sleep(0.5)
sound.tone(880,0.5)
sleep(0.5)
else:
set_color(0,100,0)
draw_text(50,140,"No problems detected")
paint_buffer()
sleep(1)
use_buffer()
while get_key() != "esc":
clear()
t=round(temp.measurement(),2)
m=mag.measurement()
Don’t let us in the car!

## Slide 18
from ti_hub import *
from ti_draw import *
flash=led("BB1")
sound=speaker("BB 2")
temp=temperature("IN 1")
mag=magnetic("IN 3")
Physical Computing …
Heat Car Alarm
Structure
Translate
Process
Control
set_color(0,0,255)
draw_text(50,80,"HEAT CAR ALARM")
set_color(0,0,0)
draw_text(50,120,"Temperature in car = {}".format(t))
if m > 100:
draw_text(50,100,"Baby not in car")
set_color(0,100,0)
draw_text(50,140,"No problems detected")
else:
draw_text(50,100,"Baby in car")
if t > 30:
set_color(255,0,0)
draw_text(50,140,"Baby in heath distress")
flash.blink(10,1)
sound.tone(440,1)
sleep(0.5)
sound.tone(880,0.5)
sleep(0.5)
else:
set_color(0,100,0)
draw_text(50,140,"No problems detected")
paint_buffer()
sleep(1)
use_buffer()
while get_key() != "esc":
clear()
t=round(temp.measurement(),2)
m=mag.measurement()
Don’t let us in the car!

## Slide 19
from ti_hub import *
from ti_draw import *
flash=led("BB1")
sound=speaker("BB 2")
temp=temperature("IN 1")
mag=magnetic("IN 3")
Physical Computing …
Heat Car Alarm
Structure
Translate
Process
Control
set_color(0,0,255)
draw_text(50,80,"HEAT CAR ALARM”)
set_color(0,0,0)
draw_text(50,120,"Temperature in car = {}".format(t))
if m > 100:
draw_text(50,100,"Baby not in car")
set_color(0,100,0)
draw_text(50,140,"No problems detected")
else:
draw_text(50,100,"Baby in car")
if t > 30:
set_color(255,0,0)
draw_text(50,140,"Baby in heat distress")
flash.blink(10,1)
sound.tone(440,1)
sleep(0.5)
sound.tone(880,0.5)
sleep(0.5)
else:
set_color(0,100,0)
draw_text(50,140,"No problems detected")
paint_buffer()
sleep(1)
use_buffer()
while get_key() != "esc":
clear()
t=round(temp.measurement(),2)
m=mag.measurement()
Don’t let us in the car!

## Slide 20
Physical Computing …
Heath Car Alarm
Don’t let us in the car!
Structure
Translate
Process
Control

## Slide 21
10 cm
Physical Computing …
Uniform Linear Motion
from time import *
from ti_system import *
import ti_rover as rv
d0=rv.ranger_measurement()
t0=clock()
dis=[] ; t=[]
rv.forward(100)
while d > 0.1:
d=rv.ranger_measurement()
dis.append(d)
t.append(clock())
rv.stop()
store_list("distance",dis) ; store_list("time",t)
store_value("t0",t0) ; store_value("d0",d0)
+ data manipulation

## Slide 22
10 cm
from time import *
from ti_system import *
import ti_rover as rv
d0=rv.ranger_measurement()
t0=clock()
dis=[] ; t=[]
rv.forward(100)
while d > 0.1:
d=rv.ranger_measurement()
dis.append(d)
t.append(clock())
rv.stop()
store_list("distance",dis) ; store_list("time",t)
store_value("t0",t0) ; store_value("d0",d0)
Physical Computing …
Uniform Linear Motion
+ data manipulation

## Slide 23
Physical Computation
in the classroom
Teaching is more than the dissemination of content
Teaching should cultivate curiosity and inquiry
Teaching should spark student imagination and creativity
Students
deserve it!
Some skills become more important because technology requires it
Some skills become less important because technology replaces it
Some skills becomes possible because technology allows it
based on Bert Waits – 2000 Co-founder Teachers Teaching with Technology™